## Slide 1: Implementation of the solver for coupled heat transfer in gas and solid
Instructors: 1) I. Marchevsky, Ph.D., Assoc.prof.
2) M. Kraposhin, Ph.D., Senior Researcher

## Slide 2: Contents
Problem description
Choice of the numerical method
Implementation
Test problems

## Slide 3: Problem description
Mach number – 0 < Ma < 5
EoS – perfect gas
Viscous flow of Newtonian media
Transient heat transfer in solid (Fourier law)

## Slide 4: Governing equations
Perfect gas
Solid
Ideal heat contact

## Slide 5: Numerical model
Space & time discretization
  Finite Volume Method – space and time divided on non-intersecting cells (intervals)
Numerical schemes
  Mean theorem + Gauss theorem
Time integration algorithm
  Operator-splitting methods like PISO or PIMPLE

## Slide 6: Models coupling
Single matrix
  Single equation of energy for both gas & solid.
  Stable and robust, but hard to implement and use.
Multiple domains, iterative coupling
  Easy to work with complex geometries, performance degradation*).
  Needs data interpolation on the interface.
*) Not very important when using operator splitting methods like PISO

## Slide 7: Implementation in OpenFOAM
Current implementation in OpenFOAM – chtMultiRegionFoam:
  Iterative solution of energy balance between several solid and fluid regions.
  Uses outer PIMPLE loop and special B.C. for coupling between domains.
List of domains managed through the regionProperties dictionary.
Connection between regions established via boundary conditions for temperature.
Main limitation – subsonic speeds of fluid (Ma<1).
Solid
Gas
Temperature
Heat flux
Temperature
Heat flux

## Slide 8: Designing new solver
https://github.com/TonkomoLLC/hybridCentralSolvers
PISO/SIMPLE/PIMPLE are known to be oscillatory at high speeds
  we need different method for flows with Ma > 1.
rhoCentralFoam was designed for flows with Ma > 1.
  it is explicit , not efficient when Ma < 1.
Solution – hybrid approach
  Combine pimpleCentralFoam and chtMultiRegionFoam
For the most general implementation, see

## Slide 9: pimpleCentralFoam
Implicit KT/KNP fluxes for advection
PIMPLE algorithm for coupling
incompressible
compressible

## Slide 10: Hybrid PIMPLE/KT algorithm
Increase current time – 1
Solve explicit equation for density – 3
Start SIMPLE loop – 4
Assemble momentum matrix – 5
If only PISO iterations, solve for energy – 7
Start PISO loop – 8
If more then 1 SIMPLE iterations, solve for energy – 9
Solve continuity equation formulated for pressure, update velocity and density with EOS – 10-14
Update blending field “kappa” – 16
Update mechanical energy transport – 17

## Slide 11: pimpleCentralFoam source code
pisoCentral/
  commonIncludes/
    Eqns
    createCommonCentralFields.H
    updateKappa.H
  kappaFunctions/
pimpleCentralFoam/
  Make/
  createFields.H
  hEqn.H
  pEqn.H
  pimpleCentralFoam.C
hybridCentralSolvers/OpenFOAM-4.1/
Library libpisoCentral.so with common operations used pimpleCentralFoam
Source code for pimpleCentralFoam solver

## Slide 12: Hybrid PIMPLE/KT algorithm sources
massEqn.H
UEqn.H
hEqn.H
pEqn.H
updateMechanicalFields.H
updateKappa.H
updateCentralWeights.H psiUpdateCentralFields.H
commonIncludes/

## Slide 13: Other hybrid PIMPLE/KT solvers
pimpleCentralDyMFoam – solver with mesh motion
rhoPimpleCentralFoam – solver for gases with equations of state, different to perfect gas
reactingPimpleCentralFoam – solver for multicomponent mixtures flow with chemical reactions
twoPhaseMixingCentralFoam – solver for two phase homogeneous liquids flows (water & air, for example)
chtMultiRegionCentralFoam – this Track solver

## Slide 14: Examples of pimpleCentralFoam solver
Supersonic jet flows
Acoustics
Plasma flows

## Slide 15: Boundary conditions
Inlet (for subsonic and supersonic flows)
Outlet – mixed subsonic/supersonic (subsonicSupersonicPressureOutlet, libcompressibleTools, can be downloaded from github.com)
Walls – adiabatic, coupled to solids

## Slide 16: Steps to develop supersonic coupled with heat transfer solver
Resulting source codes of each step stored in separate folders of training track materials
in the folder src/
https://github.com/unicfdlab/TrainingTracks/tree/master/OpenFOAM/gasThermoCoupled-OF4.1
Step 1. Create new solver and link with regionProperties to allow multiple domains in single case.
Step 2. Move fluid domain from default location to user-specified.
Step 3. Create source code to solve for heat transfer in several (solid) bodies.
Step 4. Link created code with new solver. Compile the solver.

## Slide 17: Simplifications
Single domain for fluid, multiple domains for solids
Fluid
Solid 1
Solid 2
Solid 3
Solid 4
Application: flow over several bodies, or structure composed of several materials
Benefits: No need to rewrite most of the code for gas dynamics
More general case – ToncomoLLC github page
https://github.com/TonkomoLLC/hybridCentralSolvers

## Slide 18: Simplifications - 2
Nearest cell interpolation — for meshes with relatively uniform and equal grid distribution on external boundaries
turbulentTemperatureCoupledBaffleMixed uses approximated expressions for heat fluxes to satisfy ideal heat contact condition
Domain 1
Domain 2

## Slide 19: Initialization steps
Download hybridCentralSolvers https://github.com/unicfdlab/hybridCentralSolvers
Build library and solvers: ./Allwmake
Download libcompressibleTools https://github.com/unicfdlab/libcompressibleTools
Build library ./makeLib.sh

## Slide 20: Step 1
Make a copy of pimpleCentralFoam solver, rename it to myChtPimpleCentralFoam and update its wmake settings:
mv pimpleCentralFoam.C myChtPimpleCentralFoam.C
Update Make/files
  myChtPimpleCentralFoam.C EXE = $(FOAM_USER_APPBIN)/myChtPimpleCentralFoam
Update Make/options
  hybridCentralSolvers=/path/to/library/source
  EXE_INC = \
  -I$(hybridCentralSolvers)/pisoCentral/lnInclude \
  ...
  -I$(LIB_SRC)/regionModels/regionModel/lnInclude
  ...
  EXE_LIBS = \
  ...
  -lregionModels
Include path and library of classes for handling multi-domain cases

## Slide 21: Step 1 results
After this step we have new solver “myChtPimpleCentralFoam” which can work potentially with multiple domains (meshes) simultaneously.

## Slide 22: Step 2
0/
constant/
system/
polyMesh/
0/
constant/
system/
polyMesh/
fluid/
fluid/
regionProperties rp(runTime);
To manage several domains
regionProperties object must be created in the program before executing all other mesh operations
Change space discretization storage for gas from «defaultRegion» to «fluid» region
Goal of this step is to separate mesh storage for fluid (gas) and solids. Each mesh is stored in the unique folder on HDD (and object in memory)

## Slide 23: General settings
Operations to create mesh and fields for fluid are now stored in new files
Create file createMeshes.H:
regionProperties rp(runTime);
#include "createFluidMeshes.H"
Update createFields.H:
#include "createFluidFields.H"
Update Make/options:
EXE_INC = \
…
-I./fluid
Fluid model files are stored in folder «fluid»
which is known to compiler to lookup for includes

## Slide 24: Remove LTS
Update main procedure in myChtPimpleCentralFoam.C — remove LTS *)
Start of the time step will look like:
....
while (pimple.loop())
{
#include "readAdditionalPimpleControl.H"
#include "acousticCourantNo.H"
#include "centralCompressibleCourantNo.H"
#include "readTimeControls.H"
#include "setDeltaT.H"
Add include for regionProperties class:
#include «regionProperties.H»
if (LTS)
{
…
}
*) LTS – Local Time Stepping

## Slide 25: Create fluid mesh & fields
Specify location for gas mesh
Put fluid-associated operations in separate files:
mkdir fluid; cd fluid/
mv ../hEqn.H ./
mv ../pEqn.H ./
mv ../createFields.H createFluidFields.H
touch createFluidMeshes.H
Create mesh for gas domain - createFluidMeshes.H:
const wordList fluidNames(rp["fluid"]);
autoPtr<fvMesh> fluidMeshPtr;
fluidMeshPtr.reset(
new fvMesh(
IOobject(
fluidNames[0],
runTime.timeName(),
runTime,
IOobject::MUST_READ
)
)
);
Pointer to gas mesh
fvMesh& fluidMesh = fluidMeshPtr();
fvMesh& mesh = fluidMesh;
Create reference to fluid (gas) mesh
Fluid fields are now created in
createFluidFields.H

## Slide 26: Update createFluidFields.H
#include "readAdditionalPimpleControl.H"
#include "createCommonCentralFields.H",
autoPtr<compressible::turbulenceModel> turbulence
(compressible::turbulenceModel::New(rho,U,phi,thermo));
#include "createFvOptions.H"
#include "createMRF.H"
#include "initContinuityErrs.H"
#include "readCourantType.H"
#include "markBadQualityCells.H"
#include "psiUpdateCentralFields.H"
#include "updateKappa.H"
#include "updateCentralWeights.H"
#include "createCentralCourantNo.H"
Move initialization operations related to fluid (gas) domain from myChtPimpleCentralFoam.C to createFluidFields.H:

## Slide 27: Step 2 results
At this step gas domain relocated from standard folder to location specified by user in the regionProperties dictionary.
Source code of gas dynamics equations approximation is now stored in separate folder “fluid/”.

## Slide 28: Step 3
myChtPimpleCentralFoam/
fluid/
solid/
Make/
Create source code to solve for heat transfer equations in solids and link necessary libraries to executable.
mkdir solid
Examples of the source code can be retrieved from chtMultiRegionPimpleFoam sources.
Add “includes” to main procedure (myChtPimpleCentralFoam.C):
#include "coordinateSystem.H"
#include "solidThermo.H"
Update wmake settings (Make/options):
-I$(LIB_SRC)/thermophysicalModels/ solidThermo/lnInclude \
Resulting source code structure will become:
Folder to store sources for solid body heat transfer model

## Slide 29: General solution procedure for solids
Create meshes for solids.
Create fields describing heat exchange process in solids.
Create approximations of energy balance equations in solids (matrices).
Solve matrices (equations) for energy balances for all solids.

## Slide 30: Create solid domains
const wordList solidsNames(rp["solid"]);
PtrList<fvMesh> solidRegions(solidsNames.size());
forAll(solidsNames, i)
{
solidRegions.set
(
i,
new fvMesh
(
IOobject
(
solidsNames[i],
runTime.timeName(),
runTime,
IOobject::MUST_READ
...
Unlike gas, for solids we have several computational domains and thus we have to store several meshes, several temperature fields, several thermal conductivity coefficients and so on.
Create createSolidMeshes.H:
For complete example see createSolidMeshes.H from training materials
Names for solid domains
Number of solid domains
Loop over all solid domains
For solid No. i, create mesh

## Slide 31: Create solid fields and objects
Place initialization operations in createSolidFields.H file.
For each solid we must create:
  Coordinate system transformation tensor (for anisotropic conductivity)
  PtrList<coordinateSystem> coordinates(solidRegions.size());
  Thermodynamic library
  PtrList<solidThermo> thermos(solidRegions.size());
  Volumetric heat sources (fvOptions objects)
  PtrList<fv::options> solidHeatSources(solidRegions.size());
  Porosity field
  PtrList<volScalarField> betavSolid(solidRegions.size());
  Field of anisotropic thermal diffusivity coefficient
  PtrList<volSymmTensorField> aniAlphas(solidRegions.size());

## Slide 32: Initialization of solid fields and objects
After declaration, objects are initialized (see createSolidFields.H for example) in cycle:
forAll(solidRegions, i)
{
...
thermos.set(i, solidThermo::New(solidRegions[i]));
...
solidHeatSources.set
(i,new fv::options(solidRegions[i]));
...
coordinates.set
(i,coordinateSystem::New(solidRegions[i],thermos[i]));
...
aniAlphas.set(i,new volSymmTensorField...
...
betavSolid.set(i, new volScalarField...
...
}

## Slide 33: Solution process for heat transfer in multiple solid bodies
Loop over all solids (solveSolidRegions.H)
forAll(solidRegions, i)
{
Create refernces for fields, coefficients and mesh for region No. i
#include "setRegionSolidFields.H“
Solve for energy balance for solid No. I
#include "solveSolid.H"

## Slide 34: Energy equation in solid
fvScalarMatrix hEqn
(
fvm::ddt(solidBetav,solidRho,solidH)
-
fvm::laplacian
(
solidBetav*solidThermo.alpha(),
solidH,
"laplacian(alpha,h)"
)
==
solidFvOptions(solidRho, solidH)
);
In case of isotropic material properties, energy balance in solid (in terms of enthalpy) reads:
  Change of energy in volume
  Heat flux
  Volumetric energy sources

## Slide 35: Step 3 results
Source code for simulation of heat transfer in solids using single solver was create
Simulation process includes:
  Initialization of meshes and fields for each solid: createSolidMeshes.H and createSolidFields.H
  Energy balance equation discretization and solution: files solveSolidRegions.H, setRegionSolidFields.H and solveSolid.H
Source code of heat transfer approximation for solid bodies stored in separate folder “solid/”
Though sources created, they are not linked to the main program

## Slide 36: Step 4
Put solid equations solution block in PIMPLE algorithm for coupled simulation:
  Update createMeshes.H:
  #include "createFluidMeshes.H"
  #include "createSolidMeshes.H"
  Update createFields.H:
  #include "createFluidFields.H"
  #include "createSolidFields.H"
  Update Make/options:
  EXE_INC = \
  … \
  -I./solid
  Update myChtPimpleCentralFoam.C — insert solution for heat transfer in solids in the PIMPLE algorithm

## Slide 37: Where to place solid body heat transfer block
solveSolidRegions.H
solveSolidRegions.H
Add steps to solve for
energy balance in solids before solving energy balance in fluid

## Slide 38: Final PIMPLE algorithm

## Slide 39: Compile solver
To compile solver, type
wmake
Screenshot

## Slide 40: Step 4 results
Source code for simulation of heat transfer in solid bodies added to main program.
Energy balance equations for solids are solved in PIMPLE algorithm before solving for energy balance of gas.
New solver myChtPimpleCentralFoam was compiled.

## Slide 41: Test cases
Laminar flow
Turbulent flow
Viscosity model - Sutherland
RAS simulation – k-w SST turbulence model
https://github.com/unicfdlab/TrainingTracks/tree/master/OpenFOAM/gasThermoCoupled-OF4.1/cases

## Slide 42: Run test cases
Laminar flow
Turbulent flow
Decompose regions
  decomposePar -region solid
  decomposePar -region fluid
Run cases
  mpirun -np 4 myChtPimpleCentralFoam -parallel
Reconstruct solution (if necessary)
  reconstructPar

## Slide 43: wallHeatFlux postprocessor
Source code is copied to /src
/Make/options is changed
($FOAM_APPBIN $FOAM_USER_APPBIN)
To compile: wmake libso
Run:
mpirun -np 4 wallHeatFlux -parallel -region solid
or
wallHeatFlux -region solid
Computed heat flux (wedge angle 5 deg.)
for laminar case: ~ 100 W
for turbulent case: ~ 1150 W

## Slide 44
Thank you for your attention!
All the source codes and numerical examples are available online
https://github.com/unicfdlab/